## Slide 1
Dr Amy Thompson
PDRA – VMXi Beamline – Diamond Light Source
Multi-dataset DIALS / xia2.multiplex

## Slide 2
Processing Multi-Crystal Data with xia2.Multiplex
Auto-processing Pipeline
Diffraction Images
DIALS Pipelines
Integrated dataset
xia2.multiplex
Merged multi-crystal .mtz
Integrated data
Integrated data
Integrated data
Unit cell clustering
dials.cluster_unit_cell
Laue group analysis
dials.cosym
Unit cell refinement
dials.two_theta_refine
Scaling
dials.scale
Resolution Analysis
dials.estimate_resolution
Space group analysis
dials.symmetry
ΔCC½ filtering
dials.scale
Resolution Analysis
dials.estimate_resolution
filtered.mtz
Integrated data
Integrated data
scaled.mtz
Clustering Analysis
dials.correlation_matrix
Isomorphism Analysis
dials.cosym
Identify Key Clusters
dials.correlation_matrix

## Slide 3
Clustering Methods to Achieve Isomorphous Data
Height (proportional to difference)
Dataset Number
Dendrogram Representation
Unit Cell Clustering
Good to detect structural non-isomorphism
Clusters on unit cell dimensions
Intensity-based Clustering
Good to detect differences in structurally isomorphous datasets
Clusters on pair-wise correlation coefficients
Brehm, W., Diederichs (2014). Acta. Cryst., D70, 101-109.
Achieving isomorphous data from multi-crystal collections is critical, although differences can still exist within structurally isomorphous crystals (ligand binding, alternative confirmations, etc).
First requires a known and consistent symmetry (methods from Brehm and Diederichs)

## Slide 4
After consistent symmetry determination, there are three types of clustering available:
Unit Cell Clustering
Correlation Clustering (intensity-based)
Cosine Angle Clustering (intensity-based)
Hierarchical Clustering in xia2.multiplex
Gildea, R. J. (2022). Acta. Cryst., D78, 752-769.
Diederichs, K. (2017). Acta. Cryst., D73, 286-293.
Correlation Clustering
Comparison of pairwise correlation coefficients
Does not distinguish types of error resulting in differences in intensities
Cosine Angle Clustering
Extension of correlation clustering
Separates systematic and random error
Same methods as indexing ambiguity resolution (dials.cosym)
Gildea, R. J., Winter, G. (2018). Acta. Cryst., D74, 405-410.

## Slide 5
Human insulin, porcine insulin and bovine insulin differ subtly in their amino acid sequences and readily grow high-quality, cubic, isomorphous crystals
Introducing a Test Case… Cows, Pigs and People
 | Cows | Pigs | People
Chain A Residue 8 |  |  | 
Chain A Residue 10 |  |  | 
Chain B Residue 30 (terminus) |  |  | 
Thompson, A. J. et al. (2025) Acta Cryst. D81, 278-290.

## Slide 6
Isomorphous nature of these samples evident at both cryogenic and room temperature
While subtle differences in unit cell are evident, natural spread across many crystals provides overlap, making them impossible to distinguish with unit cell-based clustering
Introducing a Test Case… Cows, Pigs and People
100 K
293 K
Thompson, A. J. et al. (2025) Acta Cryst. D81, 278-290.

## Slide 7
Can We Separate Cows, Pigs and People Using Clustering?
GITHUB LINK HERE